## Slide 1: ROTATE Instructions
Course Code: 0052
Dept. of Computer Science
Faculty of Science and Technology
Lecturer No: | 7(b) | Week No: | 10 | Semester: | Spring 24-25
Lecturer: | Sumaiya Malik; malik.sumaiya@aiub.edu |  |  |  | 
Course Title: Computer Organization and Architecture

## Slide 2: Overview: ROTATE
Rotates work like the shifts, except that when a bit Is shifted out one end of an operand it is put back in the other end.
These instructions can be used to examine and/or change bits or groups of bits.
*** Logic, shift, and rotate instructions is used to do binary and hexadecimal I/O.
The ability to read and write numbers will let us solve a great variety of problem.

## Slide 3: Rotate Instructions
The instruction ROL (rotate left) shifts bits to the left. The msb shifted into the rightmost bit.
The CF also gets the bit shifted out of the msb.
You can think of the destination bits forming a circle, with the least significant bit following the msb in the circle.
ROL destination, 1
and
ROL destination, CL

## Slide 4: Rotate Right (ROR)
The instruction ROR (rotate right) works just like ROL except that the bits are rotated to the right.
The rightmost bit is shifted into the msb, and also into the CF
ROR destination, 1
and
ROR destination, CL

## Slide 5: ROL, ROR and CF
In ROL and ROR, CF reflects the bit that is rotated out.
ROL and ROR can be used to inspect the bits in a byte or word, without changing the contents.
Example: Use ROL to count the number of 1 bits in BX, without changing BX. Put the answer in AX.
Solution:
XOR AX,AX
MOV CX,16
TOP:
ROL BX,1
JNC NEXT
INC AX
NEXT:
LOOP TOP

## Slide 6: RCL (Rotate Carry Left)
The Instruction RCL (Rotate through Carry LEFT) shifts the bits of the destination to the left.
The msb is shifted Into the CF and the previous value of CF is shifted Into the rightmost bit.
In other words, RCL works like Just like ROL, except that CF is part of the circle of bits being rotated. The syntax is:
RCL destination,1
and
RCL destination, CL

## Slide 7: RCR (Rotate Carry Right)
The Instruction RCR (Rotate through Carry RIGHT) works just like RCL except the bits are rotated to the right. The syntax is:
RCR destination,1
and
RCR destination, CL

## Slide 8: Example
Suppose DH contains 8Ah, CF= 1, and CL contains 3.
What are the values of DH and CF after the instruction RCR DH,CL is executed?

## Slide 9: Reversing Bit Pattern Application
Expectation: If AL contains 11011100, we want to make it 00111011
  Use SHL to shift the bits out the left end of AL Into CF.
  Then use RCR to move them Into the left end of another register (i.e. BL)
Run the above operation 8 times for 8 bits

## Slide 10: Binary and Hex Input & Output
Binary Input: Lets assume a program reads In a binary number from the keyboard, followed by a carriage return. [i.e. string of 0’s and 1’s]
Conversion in bit value needs to be done as soon as the input character is entered.
After that collect the bits in register.
To read a binary number from keyboard and store it in BX:

## Slide 11: Example: Process Input 110

## Slide 12: Assembly Conversion for input processing (110)

## Slide 13: Binary Output
Outputting the contents of BX in binary also involves the shift operation.
Algorithm for Binary output:
Write an assembly code to process the Binary output for this problem.

## Slide 14: Hex Input
Hex input consists of digits ("0" to "9") and letters ("A" to "F”) followed by a carriage return.
For simplicity, we will assume that
  Only uppercase letters are used, and
  The user inputs no more than four hex characters.
The process of converting characters to binary values is more Involved than it was for binary input, and BX must be shifted four times to make room for a hex value.

## Slide 15: Algorithm for hex input

## Slide 16: Example: input 6AB

## Slide 17: Assembly Code for Processing 6AB

## Slide 18: Algorithm for Hex Output

## Slide 19: Conversion of 4CA9h to Binary
Write an assembly code to process the Binary output for this problem.

## Slide 20
References
Assembly Language Programming and Organization of the IBM PC, Ytha Yu and Charles Marut, McGraw Hill, 1992. (ISBN: 0-07-072692-2).
http://faculty.cs.niu.edu/~byrnes/csci360/notes/360shift.htm

## Slide 21
Books
Assembly Language Programming and Organization of the IBM PC, Ytha Yu and Charles Marut, McGraw Hill, 1992. (ISBN: 0-07-072692-2).
Essentials of Computer Organization and Architecture, (Third Edition), Linda Null and Julia Lobur
W. Stallings, “Computer Organization and Architecture: Designing for performance”, 67h Edition, Prentice Hall of India, 2003, ISBN 81 – 203 – 2962 – 7
Computer Organization and Architecture by John P. Haynes.